## Slide 1: Collisional-Radiative Modeling of EBIT Spectra of High-Z Ions
Yuri Ralchenko
National Institute of Standards and Technology
Gaithersburg, MD 20899
ADAS Workshop, October 6-8 2011
Supported in part by the Office of Fusion Energy Sciences,
U.S. Department of Energy

## Slide 2
Electron
Beam
Ion
Trap

## Slide 3: NIST EBIT: main characteristics
Many operate, a few under construction
“Table-top” device
Low electron density
  Ne ~ 1012 cm-3
Monoenergetic electrons
  Ebeam = 1-30 keV
  Width ~ 60 eV
Localized volume
Continuous operation
~Any ion of any element
Effective injection of heavy ions (W, Hf, Ta, Au…)

## Slide 4: Physical processes in EBIT
Important
  Radiative
  Electron-impact excitation, deexcitation, ionization
  Radiative recombination
  Charge exchange
    Relative velocity and density of neutrals are not well known
Not so much…
  Three-body recombination
  Dielectronic recombination (may be accidentally important)

## Slide 5: Collisional-Radiative Modeling of High-Z Plasmas
Non-Maxwellian time-dependent CR code NOMAD
  Yu. Ralchenko and Y. Maron, JQSRT 71, 609 (2001)
  Various options for atomic data input
  Account of plasma effects
  Used for diagnostics of various plasmas (laser-produced, astrophysical, fusion, EBIT)
Atomic data from Flexible Atomic Code (FAC)
  M.F. Gu, Can. J. Phys. 86, 675 (2008)
  Relativistic model potential; Dirac equation; QED corrections
  Distorted wave approximation; Coulomb-Born
  Well suited for highly-charged high-Z ions
  Consistency: all relevant parameters in one run
Typical model for EBIT:
7-8 ions
~103 levels/ion
Several million transitions

## Slide 6: W spectra from ASDEX Upgrade tokamak (4 keV)
7.93 Å in W46+
3d10-3d94s
E2 line? M3 line?
T. Pütterich,
Ph.D. thesis (2005);
R. Neu et al,
Nuclear Fusion
45, 209 (2005)

## Slide 7: EBIT X-ray measurements (Eb ≈ 4 keV)
3-4
3d10-3d94s
Yu. Ralchenko et al, Phys. Rev. A 74, 042514 (2006)
M3
E2
M1
M3
E2
3d94s
Line intensity: I=N·A·E
I(E2):I(M3) = 4:3
Mainly Ni-like W46+
3d10
S. Loch et al, 2006:
Can M3 survive in fusion plasmas?..

## Slide 8: E2/M3 ratio is sensitive to density
E2+M3
E2/M3
E2 and M3 were recently resolved in
Clementson et al, PRA 81, 012505 (2010)

## Slide 9: Experiment vs theory (W, Ebeam = 8.8 keV)
Ions included:
[Ca]-[F]
6600 levels
Charge exchange
the only free parameter
EXP
THEO
W55+
W56+
W57+
W58+
W59+
W60+
W61+
W62+
W54+
n=3-n=3
transitions
E1 and M1
J.Phys. B 41, 021003 (2008)
Ionization balance and Te diagnostics

## Slide 10: Na-like doublet in highly-charged ions
D1
D2
2
1
5890 Å
5896 Å

## Slide 11: D-doublet in Na-like W, Hf, Ta, and Au
J.D. Gillaspy et al,
Phys. Rev. A 80,
010501 (2009)
Calculated spectrum
is convolved with the
spectrometer
efficiency curve
Eb  12 keV

## Slide 12: (Only!) M1 Lines in 3dn Ions of W
Yu.Ralchenko et al, Phys. Rev. A 83, 032517 (2011)
Co 3d9 4180 eV
Fe 3d8 4309 eV
Mn 3d7 4445 eV
Cr 3d6 4578 eV
V 3d5 4709 eV
Ti 3d4 4927 eV
Sc 3d3 5062 eV
Ca 3d2 5209 eV
K 3d 5347 eV

## Slide 13: Level grouping
Problem
too many levels per ion (~104)
Consider 3dn-1kl:
Provides sufficiently
dense representation

## Slide 14: Theory vs Experiment (E = 5.25 keV)
V
V
Ti
Cr
Cr
Cr
V

## Slide 15: Why only M1 lines?..
3p53dn+1 is too far
Branching ratios
…but allowed lines
appear at higher densities

## Slide 16: Density-Sensitive Ratios for Fusion Plasmas: Cr-like Ion

## Slide 17: Conclusions: CR modeling in EBITs
(Quasi-)Monoenergetic electrons
Low density
Eb ~ IP; in many cases cascades dominate
  Ratios of EUV lines in highly-charged high-Z ions are rather insensitive to beam energy
Charge exchange important for ionization balance
CR modeling is an essential tool for reliable identification of newly measured spectral lines
Good test for CR models to be applied in (magnetic) fusion