## Slide 1: Pressure diagnostic for the trap center of Electron beam ion trap by EUV spectroscopy
Guiyun Liang 梁贵云
National Astronomical Observatories, CAS
Beijing, China
ADAS 2014 workshop, Sep.29-30, Warsaw, Poland

## Slide 2
Outline
Brief background
EBIT and the EUV spectroscopy
Data analysis
(1) Density diagnostic
(2) Pressure diagnostic in EBIT center

## Slide 3
Epp et al. (2010) JpB; Beiersdorfer (2003) ARAA
Principle of electron beam ion trap (EBIT): electrons from electron gun is accelerated to tens of keV, then ionize material injected.
It has a powerful ability help us to benchmark theoretical model:
Produce ions of a desired charge state
Brief background

## Slide 4
Determine which lines come from which charge stage.
Study emission by selecting specific line formation processes
Liang et al. (2009) ApJ; Martínez PhD thesis (2005)

## Slide 5
However, the EBIT behavior is affected by pressure or vacuum of the trap, which is a fundamental parameter in experiments
Usually, the pressure is measured by ionization gauge method for high vacuum (10-3 —10-10 mbar):
Principle: By measuring the electrical ions produced when the gas is bombarded with electrons.
Accuracy: depends on the chemical composition of gases being measured, corrosion and surface deposits

## Slide 6
Epp PhD thesis (2007)
The central space is very small (55mm×10/3mm) to located a vacuum gauge.
It is separate from other space by cooling system and Helmholtz coils
What we measured pressure (10-8mbar) represents the value around the chamber wall.

## Slide 7
In theory, charge stage distribution will be smeared out due to the Charge-exchange between trapped ions with residual neutral gas, that can be regarded as a ‘recombination’ gauge.
The neutral density is proportional to the pressure in the trap center.

## Slide 8: X-ray on planetary/cometary atmospheres due to CX process
Observation comet and vernus Lisse et al. (1996)
Simulation of solar wind ions on Martian, Modolo et al. (2005)
What components in solar wind?
What velocity of these ions?
Where these ions from on solar surface?
Bodewits et al. (2006)

## Slide 9
Heidelberg FLASH/Tesla EBIT
EUV spectrometer
Grazing grating: 2400l/mm
CCD 2048×2048, 13.5m/pixel
Beam energies: 100 — 3000 eV
Energy step: 10 or 20 eV
Photon energies: 90 — 260 Å
Photon resolution: ~0.3 Å
Pressure: ~ 10-8 mbar
EUV spectra measurement in EBIT
Epp PhD thesis (2007)

## Slide 10
Above shows the resultant spectra of highly charged iron ions. Any analysis is based upon the good spectral modelling.

## Slide 11
Analysis model
Physics: Liang et al. (2014) ApJ
Atomic data
Approx.-coding
Output: emissivity
Fitting to obs.
Data analysis

## Slide 12
Cross section is from FAC and AUTOSTRUCTURE
Line identification

## Slide 13
Iobs() = Ai(E)()(, E)
Here, Ai(E) is the ionic abundance as a function of beam energy, () is the efficiency of the spectrometer, and (, E) is the line emissivity, where E refers to the beam energy
There is two method to generate the ‘evolution curve’ Ai(E)
Global fitting
Single line fitting
  Line emissivity:  ~ (E) or
  =AijNj
  For resonant lines, the uncertainty of (E) is within 5%
  Cascading effect will have <10% contribution for line emissivity.

## Slide 14
Adopting global fitting, at each pixel channel and at a given energy,

## Slide 15: Evolution curve of ionic fraction

## Slide 16
(e,Xq+) refers to the overlap factor between the electron beam and ions with charge of q+, the last term represent a continuous injection of neutrals with density of n0+. Charge-exchange rates depends on the relative velocity (100 eV) of recipient (ions) and donor (neutrals).
Charge state distribution

## Slide 17
EUV spectroscopic application to EBIT
1. Effective electron density in trap

## Slide 18
Line ratios involved emission lines with its upper level is dominantly populated from metastable levels
Resultant electron density is about 1012cm-3

## Slide 19
2. Overlap factor between e-beam and trapped ions
The overlap factor depends on the ionic charge

## Slide 20: The module of charge stage distribution
Plasma type:
Thermal
EBIT
EBIT/R with escape
PhiBB
CXERec

## Slide 21
Donors:
H (13.61)
He (24.59)
H2 (15.43)
CO (14.10)
CO2 (13.78)
H20 (12.56)
CH4 (12.6)
Treatment of CX cross-section:
Default is parameterized Landau-Zener approximation
Collection from published data (RARE!)
Hydrogenic model
Charge exchange

## Slide 22
2s 2p 3d
Obtain the average energy of captured nl (3d) orbital
Using parameterized MCLZ approximation obtain the nl-manifold CX cross-section
Statistical weight to get the nlJ-resolved cross-section
In Hydrogenic model:
Obtain the principle quantum number with peak fraction.
‘Landau-Zener’ weight as
Statistical weight
Si10+ projectile
2s2 2p (ground)
Smith et al. (2012)

## Slide 23
At low beam energies, the uncertainty (~10 eV) may be due to estimation of space charge potential, because only beam current at high energy recorded for #Fe1008 and #Fe1208
Monte-Carlo method is adopted to obtain optimized neutral density with 300×300 tests

## Slide 24
Fe XVIII
Fe XIX
Fe XX
Fe XXI

## Slide 25
The resultant neutral density at the trap center without consider the overlap factor between electron beam and ion cloud
At a current of 165 mA, and the beam energy 2390 eV, the largest central electron density is about 1.4×1013cm-3
An effective electron density is diagnosed to be 2.6×1012 cm-3

## Slide 26
Fe XVIII
Fe XIX
The resultant pressure in trap center is obtained, that is still higher than expectation.

## Slide 27
In the central region, NO ‘quantitative’ value available, except for a ‘qualitative’ estimation. The present diagnostic strongly depends on the underlying model. A further analysis is on-going.

## Slide 28
Coulomb heating:
Energy transfer between ions:
Ion escape (radial, axial):
Energy loss due to escaping ions:
Penetrante et al. (1991)
Vaxial=100V
Vradial

## Slide 29
Evolution of ions and ionic temperature:
Penetrate et al. PRA (1991)

## Slide 30
Summary
Brief background
EBIT and the EUV spectroscopy
Data analysis
a. Density diagnostic
b. Diagnostic for overlap factor between beam and ions
c. Diagnostic to the pressure in the EBIT center

## Slide 31
Thanks you for your attention!